## Slide 1: Modern Surveying Methods

## Slide 2: Principle of EDM
The EDM instrument sends out a modulated electromagnetic wave that travels through the air and is reflected back from the reflector at the target point. The instrument then measures the time it takes for the wave to travel from the instrument to the reflector and back again

## Slide 3: Types of EDM
EDM instruments are classified based on the type of carrier wave as
Microwave instruments
Infrared wave instruments
Light wave instruments.

## Slide 4: 1. Microwave Instruments
These instruments make use of microwaves. Such instruments were invented as early as 1950 in South Africa by Dr. T.L. Wadley and named them as Tellurometers. The instrument needs only 12 to 24 V batteries. Hence they are light and highly portable. Tellurometers can be used in day as well as in night. The range of these instruments is up to 100 km. It consists of two identical units. One unit is used as master unit and the other as remote unit. Just by pressing a button, a master unit can be converted into a remote unit and a remote unit into a master unit. It needs two skilled persons to operate. A speech facility is provided to each operator to interact during measurements.

## Slide 5: 2.Infrared wave instruments
In this instrument amplitude modulated infrared waves are used. Prism reflectors are used at the end of line to be measured. These instruments are light and economical and can be mounted on theodolite. With these instruments accuracy achieved is ± 10 mm. The range of these instruments is up to 3 km. These instruments are useful for most of the civil engineering works. These instruments are available in the trade names DISTOMAT DI 1000 and DISTOMAT DI 55.

## Slide 6: 3.Light wave instruments.
These instruments rely on propagation of modulated light waves. This type of instrument was first developed in Sweden and was named as Geodimeter. During night its range is up to 2.5 km while in day its range is up to 3 km. Accuracy of these instruments varies from 0.5 mm to 5 mm/km distance. These instruments are also very useful for civil engineering projects.

## Slide 7: Total station
Total station is a surveying equipment combination of Electromagnetic Distance Measuring Instrument and electronic theodolite. It is also integrated with microprocessor, electronic data collector and storage system. The instrument can be used to measure horizontal and vertical angles as well as sloping distance of object to the instrument.
Electronic distance measuring (EDM) instrument is a major part of total station. Its range varies from 2.8 km to 4.2 km. The accuracy of measurement varies from 5 mm to 10 mm per km measurement. They are used with automatic target recognizer. The distance measured is always sloping distance from instrument to the object.

## Slide 8: Advantages of total station
The following are some of the major advantages of using total station over the conventional surveying instruments:Field work is carried out very fast.
Accuracy of measurement is high.
Manual errors involved in reading and recording are eliminated.
Calculation of coordinates is very fast and accurate. Even corrections for temperature and pressure are automatically made.
Computers can be employed for map making and plotting contour and cross-sections. Contour intervals and scales can be changed in no time.

## Slide 9: Applications of total station
There are many other facilities available, the total station can be used for the following purposes.
Detail survey i.e., data collection.
Control Survey (Traverse).
Height measurement (Remove elevation measurement- REM).
Fixing of missing pillars (or) Setting out (or) Stake out.
Resection.
Area calculations, etc.
Remote distance measurement (RDM) or Missing line measurement (MLM).

## Slide 10: Introduction to GPS
WHAT IS GPS?
GPS stands for Global Positioning System. It is a highly accurate navigation system using signals from satellites to determine a location on the Earth’s surface, irrespective of weather conditions.
It is dependent on satellites high above the Earth which transmit signals containing the time and location of the satellite. Any ground-based receiver which receives signals from four or more GPS satellites can use navigation equations to calculate its location on the Earth’s surface. Constant signaling can then update speed and direction information for moving receivers.
GPS was originally developed for military use but since the 1990s has been open for civilian use and is now used in such common applications as mobile phones, car navigation systems, and of course surveying and mapping.

## Slide 11: How is GPS used in surveying
Surveying and mapping was one of the first commercial adaptations of GPS, as it provides a latitude and longitude position directly without the need to measure angles and distances between points.
However, it hasn’t entirely replaced surveying field instruments such as the theodolite, Electronic Distance Meter, or the more modern Total Station, due to the cost of the technology and the need for GPS to be able to ‘see’ the satellites therefore restricting its use near trees and tall buildings.
In practice, GPS technology is often incorporated into a Total Station to produce complete survey data. Receivers used for base line measurements are generally more complex and expensive than those in common use, requiring a high quality antenna.